## Slide 1
US Highway 18
From the East Junction of SD73 to West of Antelope Road/242nd Ave
Mark Malone, PE
SOUTH DAKOTA DEPARTMENT OF TRANSPORTATION

## Slide 2
Project Limits
Project Length = 11.3 Miles

## Slide 3
Involve the public in the design process
Exchange ideas – listen and discuss concerns
Provide a Project Overview
  Background Information
  Proposed Project
  Project Schedule
Gather Input and Comments
Why are we here?

## Slide 4
Narrow Shoulders – 2 & 3 feet
Narrow Right Of Way
Vertical Curves
Pavement Condition
Shallow Ditches
Snow Drifting
Highway Deficiencies

## Slide 5
Background Information
Grading in 1947
Resurfaced in 1980 & 2001

## Slide 6
Traffic
2020 Average Daily Traffic (ADT) = 565
25 Year Projected ADT = 664
13.9% Trucks

## Slide 7
5 Year Period from 2016 to 2020
  16 Reported Crashes
    9 Animal Hits
    1 Cross Centerline
    0 Overturn/Rollover
    3 Ran Off Road
    3 Other
  1 Fatality
  4 Injuries
Rural Major Arterial
  Reported Crash Rate = 2.95
  Statewide Weighted Crash Rate = 1.46
(crashes per million vehicle miles of travel)
Reported Crash History

## Slide 8
Widen Roadway – 6 feet Shoulders
Flatten Highway Curves
Replace Culverts and Fence
Vetal Improvements
  Curb and gutter
  Parking
  Lighting
New Asphalt surfacing year after construction
Proposed Improvements

## Slide 9
Proposed Typical Section

## Slide 10
To provide safe, efficient access to streets and highways
Limit number of direct accesses to major roadways
Provide adequate spacing between driveways and cross-roads
See Handout on website
Access Management

## Slide 11
Existing Width:
  100 feet
  80 to 90 feet in Vetal
Purchase additional ROW to 150 feet
Maintain Existing Width in Vetal
Purchase additional ROW around
highway embankment & pipes
Temporary Easements as
needed for construction
Right of Way (ROW)
See Handout on website

## Slide 12
Encroachments - Private Property Located Within the Public ROW
  Federal Highway Regulations
  Safety
Examples of Encroachments
  Signs
  Private Use (Parking)
  Landscaping Items
Owners of Encroachments will be Notified by the Winner Area Office
Encroachments
See Handout on website

## Slide 13
Some Utilities may need to be relocated
Utility Companies may negotiate easements with landowners as needed
Golden West Communications
LaCreek Electric
Utility Coordination
See Handout
on website

## Slide 14
Any Known Private Utilities?
  Waterlines
  Drainfields
  Septic Tanks
  Underground Storage Tanks
  Underground Power Lines
  Contact SDDOT
See Handout on website
Utility Coordination

## Slide 15
This project is being developed in accordance with applicable State and Federal environmental regulations.
In accordance with the National Environmental Policy Act of 1969 (NEPA), as amended. Coordination has been initiated with State & Federal resource agencies.
See Handout on website
Environmental, Social & Economic Concerns

## Slide 16
A cultural resources survey will be conducted.
The project is being reviewed to determine extent of impacts to wetlands, game production areas, etc.
Endangered and Threatened Species:
  Mammals: Northern Long-eared Bat
  Birds: Whooping Crane, Rufa Red Knot
  Plants: Western Prairie Fringed Orchid
  Insects: American Burying Beetle
See Handout on website
Environmental, Social & Economic Concerns

## Slide 17
1 Construction Season
Traffic maintained through the project
Slower traffic anticipated – expect delays
Pilot car & flaggers with one lane traffic at times
Width restriction
Construction/Traffic Impacts

## Slide 18
Landowner Meetings | Late Fall 2021
Final Design | 2022
ROW Acquisition Process | 2023
Construction | 2025
Estimated Cost: | $14.9 M
Dependent on Federal Funding

## Slide 19
Late Fall/Early Winter 2021
  Affected property owners will be contacted by SDDOT to schedule appointment
Held with individual landowners adjacent to the project to discuss:
  Driveway or access location/width
  Fence
  Drainage
  Temporary Easements
  ROW acquisition
Landowner Meetings
See Handout on website

## Slide 20: CONTACT INFORMATION
Comments Due July 7, 2021
Mailing Address
700 E Broadway Ave, Pierre, SD 57501
Email Address
Mark.Malone@state.sd.us
Phone Number
(605) 773 5409
Website (Project Information)
https://dot.sd.gov/projects-studies/projects/public-meetings